## Slide 1: Architectural Modeling and Analysis for Safety Engineering (AMASE)
Danielle Stewart
Oral Preliminary Exam
September 2018
  Model-based safety analysis of critical systems

## Slide 2: Motivation
Requirements and
Design Documents
Safety
Analyst A
Safety
Analyst B
System Safety Analysis is
- Based on Informal Specifications
- Highly Dependent on Skill of the Analyst
Notes: Safety engineers do most of the analysis activities like fault tree creation manually, based on a lot of informal requirements and design documents. These analyses seem to be quite subjective and highly dependent on the skill and experience of the safety engineers. Thus, it is not surprising that different safety engineers will quite often produce fault trees, which may differ in substantial ways. It is only through a rigorous review process that a concensus will be built on the correct fault tree, which captures the right fault behavior. We think that the review process implicitly consolidates existing information from various documents and then completes it with unspecified details architectural and fault behaviors. It would be great if all these activities would be based off a comprehensive system architecture.
We also observe that due to the complexity of the systems involved, it is possible that the fault trees may not capture involved fault scenarios that may occur due to complex interactions between components.

## Slide 3: Model-Based Development
We Base the Entire
Development Cycle
Around the Model
Why Not the
Safety Analysis?

## Slide 4: Model-Based Safety Analysis
Add Fault Model for Physical System
Power A
Pedal 1
Feed back
Plant
Fault Tolerant
Control Unit
( BSCU )
Braking System
System
A
Power B
Pedal 2
System
B
Plant
Model
AntiSkid
Command
Braking
+
AntiSkid
Command
Green Pump
Blue Pump
Isolation Valve
Isolation Valve
Shut
Normal
System
N
O
R
M
A
L
A
L
T
E
R
N
A
T
E
Accumulator
Pump
Meter
Valve
Meter
Valve
Meter
Valve
Accumulator
Valve
Mechanical
Pedal
Selector Valve
Model the Digital Controller Architecture
Automation Enables “What-If” Consideration of System Designs
and Digital Controller Architecture
Integrates System and Safety Engineering About a Common Model
and the Physical System
Wheel Braking System
AIR6110
CONTIGUOUS AIRCRAFT/SYSTEM DEVELOPMENT PROCESS EXAMPLE
Notes: Steve’s slide

## Slide 5: Conceptions of MBSA
Error propagations:
Failure Logic Modeling (FLM)
Failure Effect Modeling (FEM)

## Slide 6: Conceptions of MBSA
Failure propagations:
Failure Logic Modeling (FLM)
Failure Effect Modeling (FEM)
Directional vs Bidirectional flows

## Slide 7: Conceptions of MBSA
Failure propagations:
Failure Logic Modeling (FLM)
Failure Effect Modeling (FEM)
Directional vs Bidirectional flows
Purpose Built Fault Model vs Extension of System Model

## Slide 8: Conceptions of MBSA
Failure propagations:
Failure Logic Modeling (FLM)
Failure Effect Modeling (FEM)
Directional vs Bidirectional flows
Purpose Built Fault Model vs Extension of System Model
Compositional Analysis or Monolithic Analysis

## Slide 9: Existing Tools and Methods
 | FLM | FEM : Directional | FEM: Bidirectional | M | C | PB | ESM
EMV2 |  |  |  |  |  |  | AADL
Compass |  |  |  |  |  |  | SLIM
SmartIFlow |  |  |  |  |  |  | 
SAML |  |  |  |  |  |  | 
AltaRica |  |  |  |  |  |  | 
HipHops |  |  |  |  |  |  | East-ADL

## Slide 10: Where does the Safety Annex fit?
Extend System Model
Compositional Analysis
Implicit Failure Propagation (FEM)

## Slide 11: Existing Tools and Methods
 | FLM | FEM : Directional | FEM: Bidirectional | M | C | PB | ESM
EMV2 |  |  |  |  |  |  | AADL
Compass |  |  |  |  |  |  | SLIM
SmartIFlow |  |  |  |  |  |  | 
SAML |  |  |  |  |  |  | 
AltaRica |  |  |  |  |  |  | 
HipHops |  |  |  |  |  |  | East-ADL
Safety Annex |  |  |  |  |  |  | AADL

## Slide 12: Creation of Nominal System Model
Power A
Pedal 1
Feed back
Plant
Fault Tolerant
Control Unit
( BSCU )
Braking System
System
A
Power B
Pedal 2
System
B
Model of the Digital System
Plant
Model
AntiSkid
Command
Braking
+
AntiSkid
Command
Green Pump
Blue Pump
Isolation Valve
Isolation Valve
Shut
Normal
System
N
O
R
M
A
L
A
L
T
E
R
N
A
T
E
Accumulator
Pump
Meter
Valve
Meter
Valve
Meter
Valve
Accumulator
Valve
Mechanical
Pedal
Selector Valve
Power A
Pedal 1
Feed back
Plant
Fault Tolerant
Control Unit
( BSCU )
Braking System
Power B
Pedal 2
System
B
Model of the Digital System +
Model of the Mechanical System
Verify safety properties of the nominal digital system
Verify safety properties of the nominal mechanical system

## Slide 13: Wheel Brake System

## Slide 14: Architecture Analysis and Design Language (AADL)
AADL = SAE AS5506 standard
Target: Embedded, real-time, distributed systems
Describes both hardware and software
Extensible syntax (annex)
Open source tools, supported by SEI

## Slide 15: WBS AADL Model

## Slide 17: Architecture Modeling and Analysis Tools
Trusted
Build
Architecture Translation
seL4
eChronos
VxWorks
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
Architecture Analysis
Architecture Models
OSATE
Resolute
AGREE
SIM
Kind/JKind
Model Checker
TCG
Notes: START AGREE HERE

## Slide 18: AGREE: Assume Guarantee Reasoning Environment
Each component has a contract consisting of assumptions and guarantees
  Assumptions: Constraints over what a component expects from its environment
  Guarantees: Constraints over how a component behaves in response to its environment (requirements)
The contract of a component abstracts the behavior of its implementation
AGREE analysis
Component
Implementation
contract
contract
contract
contract
contract
contract
contract

## Slide 19
Compositional verification tool for analysis of AADL system models
AGREE: Assume-Guarantee Reasoning Environment
Focus on system safety properties
Compositional approach scales model checking to larger systems
Compositional Verification of Critical Systems
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
FCC
FCC
FCC
FCC
DaC
DaC
DaC
DaC
AFDX or
TTE
Switch
AFDX or
TTE
Switch
Example system: Quad-redundant flight control system provided by NASA

## Slide 20
Compositional verification tool for analysis of AADL system models
AGREE: Assume-Guarantee Reasoning Environment
Focus on system safety properties
Compositional approach scales model checking to larger systems
Compositional Verification of Critical Systems
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
FCC
FCC
FCC
FCC
DaC
DaC
DaC
DaC
AFDX or
TTE
Switch
AFDX or
TTE
Switch
Example system: Quad-redundant flight control system provided by NASA

## Slide 21
Compositional verification tool for analysis of AADL system models
AGREE: Assume-Guarantee Reasoning Environment
Focus on system safety properties
Compositional approach scales model checking to larger systems
Compositional Verification of Critical Systems
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
FCC
FCC
FCC
FCC
DaC
DaC
DaC
DaC
AFDX or
TTE
Switch
AFDX or
TTE
Switch
Example system: Quad-redundant flight control system provided by NASA

## Slide 22
Nominal Model Component in AADL and AGREE
Notes: Maybe remove, check on other agree slides

## Slide 23
Wrap nominal component in fault
Watch behavior of system through AGREE contracts
Creation of the Fault Model

## Slide 24
Component A
Component B
Out
In
Component A
Component B
Out
In
Nominal Behavior:
Fault Behavior:
Fault

## Slide 25: WBS Top Level Property : No inadvertent braking
Normal Operating Mode:
Mechanical pedal pressed (brakes commanded)
Sensor on pedal converts to electrical signal
Signal sent to BSCU to command brakes

## Slide 26: A Fault on the Pedal Sensor Component

## Slide 27: Behavioral Fault Propagation

## Slide 28: Active Sensor Fault
Mechanical pedal is not pressed
Inverted Boolean failure on sensor activated
Electrical signal is true and braking is commanded through BSCU
Top level lemma fails (Unintentional braking occurs)

## Slide 29: Maximum Fault vs Probabilistic Analysis
. . .
. . .

## Slide 30: Maximum Fault vs Probabilistic Analysis
. . .
. . .

## Slide 31: Maximum Fault vs Probabilistic Analysis
. . .
. . .

## Slide 32: Maximum Fault vs Probabilistic Analysis
. . .
. . .

## Slide 33: Current Support
Maximum number of faults
Probabilistic analysis
Hardware and software faults

## Slide 34: Future Work
Compositional Fault Tree Generation
Monolithic
Contracts and Faults
from Leaf Level
are used to find Minimal Cut Sets.

## Slide 35
Layer 2
Layer 3
Layer 4
Leaf Level
Top Level Safety Pröperty
Leaf Level
Contracts
Leaf level faults
Monolithic
Contracts and Faults
from Leaf Level
are used to find Minimal Cut Sets.

## Slide 36
Layer 2
Layer 3
Layer 4
Leaf Level
Top Level Safety Pröperty
Leaf Level
Contracts
Leaf level faults
Compositional
Contracts and Faults
from Leaf Level
are used to find Minimal Cut Sets for the next highest layer.

## Slide 37
Layer 2
Layer 3
Layer 4
Leaf Level
Top Level Safety Pröperty
Leaf Level
Contracts
Leaf level faults
Compositionality
Layer 4
Contracts
Compositional
Contracts and Faults
from Leaf Level
are used to find Minimal Cut Sets for the next highest layer.

## Slide 38
Layer 2
Layer 3
Layer 4
Top Level Safety Pröperty
Layer 4 faults
Compositionality
Layer 4
Contracts
Layer 3
Contracts
Compositional
Contracts and Faults
from Leaf Level
are used to find Minimal Cut Sets for the next highest layer.

## Slide 39
Layer 2
Layer 3
Top Level Safety Pröperty
Layer 3 faults
Compositionality
Layer 2
Contracts
Layer 3
Contracts
Compositional
Contracts and Faults
from Leaf Level
are used to find Minimal Cut Sets for the next highest layer.

## Slide 40: Future Work
Compositional Fault Tree Generation
Byzantine Faults
Transient Faults Analysis