## Slide 1: The Safety Annex for AADL and the Safety Assessment Process
University of Minnesota
Danielle Stewart
  Model-based safety analysis of highly complex safety critical systems

## Slide 2: Traditional Safety Assessment Process
System engineers develop architecture and related documentation (signal flow diagrams, etc.)
Safety Analysts use this information to develop hazard (FHA) and safety assessments (PSSA)
Given safety assessment findings, changes to the architecture are proposed.
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 3: Traditional Safety Assessment Process
Problems with the traditional approach:
Architectural details about the system behavior gathered from multiple sources
Investigation typically stops at system level, software function details largely unexplored
Lack of precise models of the system architecture and its failure modes
Changes can be made in the system architecture that are not reflected in the safety assessment
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 4: Model Based Safety Assessment Process
Use single unified model to support both system design and safety analysis
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 5: Model Based Safety Assessment Process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and minimal cut sets produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 6: Architecture Analysis and Design Language (AADL)
AADL = SAE AS5506 standard
Target: Embedded, real-time, distributed systems
Describes both hardware and software
Extensible syntax (annex)
Open source tools, supported by SEI

## Slide 7: Architecture Modeling and Analysis Tools
Trusted
Build
Architecture Translation
seL4
eChronos
VxWorks
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
Architecture Analysis
Architecture Models
OSATE
Resolute
AGREE
SIM
Kind/JKind
Model Checker
TCG
Notes: START AGREE HERE

## Slide 8
Compositional verification tool for analysis of AADL system models
AGREE: Assume-Guarantee Reasoning Environment
Focus on system safety properties
Compositional approach scales model checking to larger systems
Compositional Verification of Critical Systems
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
FCC
FCC
FCC
FCC
DaC
DaC
DaC
DaC
AFDX or
TTE
Switch
AFDX or
TTE
Switch
Example system: Quad-redundant flight control system provided by NASA

## Slide 9: AGREE: Assume Guarantee Reasoning Environment
Each component has a contract consisting of assumptions and guarantees
  Assumptions: Constraints over what a component expects from its environment
  Guarantees: Constraints over how a component behaves in response to its environment (requirements)
AGREE analysis
Component
Implementation
contract
contract
contract
contract
contract
contract
contract

## Slide 10: Safety Annex for AADL
Define faults on component output
Behavioral propagation through AGREE contracts
Independence or dependence between faults can be captured
Generates output such as:
  Counterexamples showing active faults and how they propagate
  Probabilistic analysis using a probability threshold
  Minimal Cut Sets in terms of cardinality or probability
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 11: Safety Annex
Safety syntax is incorporated as an annex of AADL

## Slide 12: Behavioral Failure Propagation
Wrap nominal component output in fault
Watch behavior of system through AGREE contracts when fault is activated
Component A
Component B
Out
In
Component A
Component B
Out
In
Nominal Behavior:
Fault Behavior:
Fault

## Slide 13: Wheel Brake System : Preliminary System Diagram

## Slide 14: Wheel Brake System AIR6110
FBK: AIR6110 Case Study
Notes: The large WBS example.

## Slide 15: MBSA Steps: WBS and AADL/AGREE/Safety Annex
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and minimal cut sets produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 16: System Architecture in AADL

## Slide 17: WBS Architecture
30 different types of components
169 component instances

## Slide 18: MBSA Steps: WBS and AADL/AGREE/Safety Annex
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and minimal cut sets produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 19: Top Level Safety Properties

## Slide 20: Nominal Model Analysis Output

## Slide 21: MBSA Steps: WBS and AADL/AGREE/Safety Annex
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and minimal cut sets produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 22: Defining Faults on Component Outputs
Valves
  Stuck open
  Stuck closed
  Stuck nondeterministically
Sensors
  Output inverted
Pumps
  Output zero
Calculating components and Gates
  Erroneous data

## Slide 23: A Fault Definition
Selector Valve
Blue pump in
Green pump in
Blue line out
(blue_select_out)
Green line out

## Slide 24: Fault Node Definition
Fault node defines behavior of fault when activated
Commonly used fault nodes held in library
Users can define nodes specific to a domain

## Slide 25: MBSA Steps: WBS and AADL/AGREE/Safety Annex
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and minimal cut sets produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 26: Specify Fault Hypothesis Statement
Located in system implementation
Max N Fault Analysis
Probabilistic Analysis
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 27: MBSA Steps: WBS and AADL/AGREE/Safety Annex
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and minimal cut sets produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 28: Analysis Results
Max 1 Fault Analysis:
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 29: Counterexample View

## Slide 30: MBSA Steps: WBS and AADL/AGREE/Safety Annex
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and minimal cut sets produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 31: Safety Annex Approach

## Slide 32: MBSA Steps: WBS and AADL/AGREE/Safety Annex
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and minimal cut sets produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 33: Design Change Option
Redundancy in the Pedal Sensor
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 34: Results of Design Change
Now resilient against this fault
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.

## Slide 35: Minimal Cut Set Analysis
The minimal sets of fault combinations that cause violation of the safety property.
Used in Fault Tree Analysis for PSSA/SSA.
Gives insight into problematic subcomponents of the system, single points of failure, etc.
Results from Safety Annex comes in 3 forms:
Tally of how many cut sets with certain cardinality
Text file giving description of each cut set, what component they effect, and which faults are in the sets
SOTERIA input file used to generate graphical fault trees

## Slide 36: Byzantine Fault Modeling

## Slide 37: Future Work
Use the information gleaned from the compositional collection of minimal cut sets for interesting things:
  Use fault probabilities to calculate the system threshold
Plans for use in a large scale aircraft system in 2020

## Slide 38: Questions?
Fault Modeling
MBSA Approach
Safety Assessment Process