## Slide 1: Architectural Modeling and Analysis for Safety Engineering (AMASE)
Year-end Review
4 Oct 2018
Research Opportunities in Aeronautics (NRA ROA-2015)
  Model-based safety analysis of highly complex safety critical systems

## Slide 2: Motivation
Requirements and
Design Documents
Safety
Analyst A
Safety
Analyst B
System Safety Analysis is
- Based on Informal Specifications
- Highly Dependent on Skill of the Analyst
Notes: Safety engineers do most of the analysis activities like fault tree creation manually, based on a lot of informal requirements and design documents. These analyses seem to be quite subjective and highly dependent on the skill and experience of the safety engineers. Thus, it is not surprising that different safety engineers will quite often produce fault trees, which may differ in substantial ways. It is only through a rigorous review process that a concensus will be built on the correct fault tree, which captures the right fault behavior. We think that the review process implicitly consolidates existing information from various documents and then completes it with unspecified details architectural and fault behaviors. It would be great if all these activities would be based off a comprehensive system architecture.
We also observe that due to the complexity of the systems involved, it is possible that the fault trees may not capture involved fault scenarios that may occur due to complex interactions between components.

## Slide 3: Model-Based Development
We Base the Entire
Development Cycle
Around the Model
Why Not the
Safety Analysis?

## Slide 4: Model-Based Safety Analysis
Add Fault Model for Physical System
Power A
Pedal 1
Feed back
Plant
Fault Tolerant
Control Unit
( BSCU )
Braking System
System
A
Power B
Pedal 2
System
B
Plant
Model
AntiSkid
Command
Braking
+
AntiSkid
Command
Green Pump
Blue Pump
Isolation Valve
Isolation Valve
Shut
Normal
System
N
O
R
M
A
L
A
L
T
E
R
N
A
T
E
Accumulator
Pump
Meter
Valve
Meter
Valve
Meter
Valve
Accumulator
Valve
Mechanical
Pedal
Selector Valve
Model the Digital Controller Architecture
Automation Enables “What-If” Consideration of System Designs
and Digital Controller Architecture
Integrates System and Safety Engineering About a Common Model
and the Physical System
Wheel Braking System
AIR6110
CONTIGUOUS AIRCRAFT/SYSTEM DEVELOPMENT PROCESS EXAMPLE
Notes: Steve’s slide

## Slide 5
Nominal Model
Notes: Maybe remove, check on other agree slides

## Slide 6: Creation of Nominal System Model
Power A
Pedal 1
Feed back
Plant
Fault Tolerant
Control Unit
( BSCU )
Braking System
System
A
Power B
Pedal 2
System
B
Model of the Digital System
Plant
Model
AntiSkid
Command
Braking
+
AntiSkid
Command
Green Pump
Blue Pump
Isolation Valve
Isolation Valve
Shut
Normal
System
N
O
R
M
A
L
A
L
T
E
R
N
A
T
E
Accumulator
Pump
Meter
Valve
Meter
Valve
Meter
Valve
Accumulator
Valve
Mechanical
Pedal
Selector Valve
Power A
Pedal 1
Feed back
Plant
Fault Tolerant
Control Unit
( BSCU )
Braking System
Power B
Pedal 2
System
B
Model of the Digital System +
Model of the Mechanical System
Verify safety properties of the nominal digital system
Verify safety properties of the nominal mechanical system

## Slide 7: Wheel Brake System

## Slide 8: Architecture Analysis and Design Language (AADL)
AADL = SAE AS5506 standard
Target: Embedded, real-time, distributed systems
Describes both hardware and software
Extensible syntax (annex)
Open source tools, supported by SEI

## Slide 9: WBS AADL Model

## Slide 11: Architecture Modeling and Analysis Tools
Trusted
Build
Architecture Translation
seL4
eChronos
VxWorks
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
Architecture Analysis
Architecture Models
OSATE
Resolute
AGREE
SIM
Kind/JKind
Model Checker
TCG
Notes: START AGREE HERE

## Slide 12: AGREE: Assume Guarantee Reasoning Environment
Each component has a contract consisting of assumptions and guarantees
  Assumptions: Constraints over what a component expects from its environment
  Guarantees: Constraints over how a component behaves in response to its environment (requirements)
The contract of a component abstracts the behavior of its implementation
AGREE analysis
Component
Implementation
contract
contract
contract
contract
contract
contract
contract

## Slide 13
Compositional verification tool for analysis of AADL system models
AGREE: Assume-Guarantee Reasoning Environment
Focus on system safety properties
Compositional approach scales model checking to larger systems
Compositional Verification of Critical Systems
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
FCC
FCC
FCC
FCC
DaC
DaC
DaC
DaC
AFDX or
TTE
Switch
AFDX or
TTE
Switch
Example system: Quad-redundant flight control system provided by NASA

## Slide 14
Compositional verification tool for analysis of AADL system models
AGREE: Assume-Guarantee Reasoning Environment
Focus on system safety properties
Compositional approach scales model checking to larger systems
Compositional Verification of Critical Systems
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
FCC
FCC
FCC
FCC
DaC
DaC
DaC
DaC
AFDX or
TTE
Switch
AFDX or
TTE
Switch
Example system: Quad-redundant flight control system provided by NASA

## Slide 15
Compositional verification tool for analysis of AADL system models
AGREE: Assume-Guarantee Reasoning Environment
Focus on system safety properties
Compositional approach scales model checking to larger systems
Compositional Verification of Critical Systems
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
FCC
FCC
FCC
FCC
DaC
DaC
DaC
DaC
AFDX or
TTE
Switch
AFDX or
TTE
Switch
Example system: Quad-redundant flight control system provided by NASA

## Slide 16
Notes: Maybe remove, check on other agree slides

## Slide 17
Fault Model
Notes: Maybe remove, check on other agree slides

## Slide 18
Wrap nominal component in fault
Watch behavior of system through AGREE contracts

## Slide 19
Component A
Component B
Out
In
Component A
Component B
Out
In
Nominal Behavior:
Fault Behavior:
Fault

## Slide 20: Safety Annex
Safety syntax is incorporated as an annex of AADL

## Slide 21: WBS : No inadvertent braking
Normal Operating Mode:
Mechanical pedal pressed (brakes commanded)
Sensor on pedal converts to electrical signal
Signal sent to BSCU to command brakes

## Slide 22: A Fault on the Pedal Sensor Component

## Slide 23: Behavioral Fault Propagation

## Slide 24: Active Sensor Fault
Mechanical pedal is not pressed
Inverted Boolean failure on sensor activated
Electrical signal is true and braking is commanded through BSCU
Top level lemma fails (Unintentional braking occurs)

## Slide 25: Maximum Number of Faults (Compositional)

## Slide 26: Probabilistic Analysis (Monolithic)

## Slide 27: Hardware Dependent Faults
Fault in HW triggers faults in connected components

## Slide 28: Hardware Dependent Faults
  HW fault definition in the Fault Statement of the component type

## Slide 29: Hardware Dependent Faults
  HW propagation in the Safety Annex of the component implementation

## Slide 30: Byzantine Faults Simulation: Flight Control Computer
Created multiple connections to observers
Introduced disagreement through fault injection

## Slide 31: Cut Set Generation
Standards (APR4761, AIR6110, etc) describe techniques involving cut sets
Required for FTA and FMEA
Currently, these are the needs of Safety Engineers in a Safety Analysis tool

## Slide 32: Inductive Validity Cores

## Slide 33: Inductive Validity Cores
Safety Property

## Slide 34: Inductive Validity Cores
Safety Property
a
b
c
d
e
f
Model Elements

## Slide 35: Inductive Validity Cores
Safety Property
a
b
c
d
e
f
Model Elements: {a,b,c,d,e,f}

## Slide 36: Inductive Validity Cores
Safety Property
a
b
c
d
e
f
IVC : A minimum set of elements
needed to prove the
Safety Property
{a, c, d}

## Slide 37: Inductive Validity Cores
Safety Property
a
b
c
d
e
f
All IVCs : All minimal sets of elements
needed to prove the
Safety Property
{ {a,c,d}, {b,e}, {f} }

## Slide 38: Inductive Validity Cores with Faults
Safety Property
Model Elements : {Faults = FALSE, Guarantees}

## Slide 39: Cut Set Generation: Inductive Validity Cores with Faults
Safety Property
IVCs : { {, ,

## Slide 40: Cut Set Generation: Inductive Validity Cores
Safety Property
Model Elements