## Slide 2
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Verify that the nominal model supports the requirements using formal verification
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults through formal verification, using system traces and minimal cut sets produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Starts
Ends
Notes: This figure presents our proposed use of this shared system design and safety analysis
model in the context of the ARP4754A Safety Assessment Process Model (derived from
Figure 7 of ARP4754A). The shared model is one of the system development artifacts
from the “Development of System Architecture” and “Allocation of System Requirements
to Item” activities in the System Development Process, which interacts with the
PSSAs and SSAs activities in the Safety Assessment Process. The shared model can
serve as an interface to capture the information from the system design and implementation
that is relevant for the safety analysis.